        Adding a Power On/Off Button to Pi

- When powered and shutdown, shorting the pin GPIO3 with GND will wake up the Pi. This is an inbuilt feature available in all models of Raspberry Pi. Therefore, this is the wake up functionality.
- For implementing the sleep functionality, configure the pin GPIO3 as an interrupt pin that detects falling edge. The script that does this is ListenForShutdown.py.
- This file should be placed in the directory /etc/local/bin and should be made executable using the following command
  sudo chmod +x /usr/local/bin/ListenForShutdown.py
- We should have a provision to start and stop this service. This is done by the script ListenForShutdown.py. This should be placed in the directory /etc/init.d and should be made executable using the following command

        sudo chmod +x /etc/init.d/ListenForShutdown.sh

This script should be registered to run on boot. Execute

        sudo update-rc.d ListenForShutdown.sh defaults

- By default, the service will be running.
- To stop, use

        sudo /etc/init.d/ListenForShutdown start

To start, use

        sudo /etc/init.d/ListenForShutdown stop

An alias can be created and added to the .bash_aliases file to make it shorter.